## Slide 1: Socket Communication using AT Commands

## Slide 2: What is Socket Communication?
• TCP/IP communication over GSM/GPRS/LTE networks.
• Enables IoT devices to connect to internet servers.
• Used for data logging, remote monitoring, and control.

## Slide 3: Why Use AT Commands?
• AT commands allow control of GSM modules without complex programming.
• Easy to send commands over serial interface (UART).
• Widely supported by modules like Cavli C10GS, C16QS, etc.

## Slide 4: Key AT Commands
• AT+QIOPEN - Open TCP/UDP socket.
• AT+QISEND - Send data over socket.
• AT+QICLOSE - Close the socket connection.
• Requires PDP context to be activated before opening socket.

## Slide 5: Example Command Sequence
1. Attach to network: AT+CGATT=1
2. Define PDP context: AT+CGDCONT=1,"IP","your.apn.here"
3. Activate PDP: AT+QIACT=1
4. Open Socket: AT+QIOPEN=1,0,"TCP","example.com",80,0
5. Send Data: AT+QISEND=0,length
6. Close Socket: AT+QICLOSE=0

## Slide 6: Cavli Module Examples
• Cavli modules supporting TCP/IP sockets:
- C10GS
- C16QS
- C42QM

## Slide 7: Conclusion
• AT commands like AT+QIOPEN, AT+QISEND, and AT+QICLOSE enable TCP socket communication.
• Useful for IoT devices needing internet connectivity over GSM/LTE.